## Slide 1: Dirt

## Slide 2: clay
Clay is a naturally occurring material composed primarily of fine-grained minerals, which show plasticity through a variable range of water content, and which can be hardened when dried and/or fired.
Composition: Al, Si and O plus water (and other elements sometimes)
Why use clay? To begin with it’s made of the most abundant elements
www.geology.ar.gov

## Slide 3: clay
Properties
  Plasticity (manipulate at room temperature)
    First material to be easily manipulated into complex shapes
  Cohesion
    Maintains shape
  High strength in compression (after drying, baking)
    Poor strength in tension
  Opaque
  Insulating
  Can be Chemically transformed
    Upon heating to above 1000°C
    Remove water
    But also induce formation of a chemical bond
    Shrinks upon firing
    Called a ceramic after firing

## Slide 4: Clay structure
Properties:
With water layers can slide past each other, which leads to
 plasticity
Upon drying the clay it will harden but no chemical reaction is induced, which leads to  sundried bricks
Upon firing (>1000°C) can induce chemical bonding of the layers
(formation of Si-O-Si bonds), which leads to  Ceramics
Silica, Aluminum atom
Aluminum or Magnesium
Oxygen atom
Hydroxyl group

## Slide 5: Clay structure
Properties:
With water layers can slide past each other, which leads to
 plasticity
Upon drying the clay it will harden but no chemical reaction is induced, which leads to  sundried bricks
Upon firing (>1000°C) can induce chemical bonding of the layers
(formation of Si-O-Si bonds), which leads to  Ceramics
SEM Image of Kaolinite 1350X

## Slide 6: Where does Clay come from?
Form from weathering of rocks
  Weak acids dissolve silicate bearing rocks
  Clays defined by size <2µm (<0.0002cm in diameter)
  Doesn’t naturally settle
  Silt is larger
Primary clays found at site of formation, secondary clays washed downstream
Clays have many different types
  Depends on the minerals in the soil
  Lots of clay formed after glaciation
  Examples: Kaolinite and Smectite

## Slide 7: Types of Clay
Kaolinite (1 part Al2O3 and 2 parts SiO2 and 2 H2O)
  1:1 (1 tetrahedra layer then 1 octahedra layer)
  Also called china Clay
  Low shrink-swell capacity
  Heat below 550°C and its reversible drying
  Heat above 1000°C and you make stoneware dishes
  Used in porcelain, toothpaste, cosmetics, paint, organic farming, Kaopectate, Quick-clot combat gauze.

## Slide 8: Types of Clay
Smectite Clay
  Montmorillonite most common form
  2:1 (2 tetrahedra:1 octahedra) (1T:1O:1T)
  Opposite of Kaolinite it has a large shrink-swell capacity
  Used in oil drilling, cores of dams, liners in landfills, cat litter, can cause micelles to assemble into vesicles, look like cell membranes. It also helps nucleotides assemble into RNA which will end up inside the vesicles. These are the building blocks of early lifeforms.

## Slide 9: Clay structure
Kaolinite
Montmorillonite

## Slide 10: Clay structure
So which is this?
Silica, Aluminum atom
Aluminum or Magnesium
Oxygen atom
Hydroxyl group
Tetrahedra
Octahedra
Tetrahedra
Montmorillonite

## Slide 11: Early History of Clay
Paleolithic (2.5M to 15,000 years ago)
  26,000 years ago Central Europe
  Clay figurines (Venus)
  Many were broken (performance art?)
Mesolithic (15,000-11,000 years ago)
  Japanese pottery

## Slide 12: Earliest Clay Pottery
Jomon People of Japan
  16,000 years ago
  Hunter gatherers who carried clay pots for cooking
Incipient Jōmon Pottery (14,000–8000 BC) Tokyo National Museum, Japan.
http://en.wikipedia.org/wiki/J%C5%8Dmon_period#Earliest_pottery

## Slide 13: Early History of Clay
Paleolithic (2.5M to 15,000 years ago)
  26,000 years ago Central Europe
  Clay figurines (Venus)
  Many were broken (performance art?)
Mesolithic (15,000-11,000 years ago)
  Japanese pottery
Neolithic (~10,000 to 5000 years ago) (8000-3000BC)
  10,000BC Natufians (Israel/ Jerico) clay bricks

## Slide 14: Mesopotamia
Jericho
10,000BC
Notes: Fix placement of pins for Catal Huyuk, Jericho, and Sumar; It looks off to me -Van

## Slide 15: Jericho
One of the oldest inhabited city in the world
Built 12,000 years ago
Sun baked bricks, still hunting and gathering
By 10,000 year ago, Crops cultivated and stored in clay
http://en.wikipedia.org/wiki/Jericho#Ancient_period

## Slide 16: Clay Sickle
Sumarian
3000BC
For harvesting Wheat
http://commons.wikimedia.org/wiki/File:ClaySumerianSickle.jpg

## Slide 17: Early History of Clay
Paleolithic (2.5M to 15,000 years ago)
  26,000 years ago Central Europe
  Clay figurines (Venus)
  Many were broken (performance art?)
Mesolithic (15,000-11,000 years ago)
  Japanese pottery
Neolithic (~10,000 to 5000 years ago) (8000-3000BC)
  10,000BC Natufians (Israel/ Jerico) clay bricks
  7000-5000BC Catal Huyuk clay society
  6000BC rise of Mesopotamia/ Sumarians
  5000-4000BC potters wheel
  4000BC Cuneiform clay tablets/ writing
  Track trade, land ownership, centralized government

## Slide 18: Mesopotamia
Jericho
10,000BC
Catal Huyuk
7000BC -5000BC
Sumar
5000BC-2000BC
Notes: Fix placement of pins for Catal Huyuk, Jericho, and Sumar; It looks off to me -Van

## Slide 19: Cuneiform
Epic of Gilgamesh
Oldest written story
2700BC
Discovered in 1853
12 tablets
Account of the adventures of the king of Ur who lived in ancient Mesopotamia as he discovers why he can’t be immortal among other things
http://static.newworldencyclopedia.org/thumb/2/26/GilgameshTablet.jpg/250px-GilgameshTablet.jpg

## Slide 20: Ancient Uses
Building Materials

## Slide 21: Clay for construction
Great Ziggurat of Ur (modern Iraq) (2000BC)
Built of clay and mud

## Slide 22: Ancient Uses
Building Materials
Writing materials
Cooking materials
Storage materials
Sling Ammunition
Medical
  Armenian bole
    (early version of Milk of Magnesia for upset stomach)
Musical Instruments
  Ocarina
https://s-media-cache-ak0.pinimg.com/236x/42/12/96/421296210e9c55b6fbae0c5dab43bf8f.jpg

## Slide 23: Ocarina?
How about more recent music?
  Anyone recognize this song?
  Ocarina Solo

## Slide 24: Modern Uses
Clay
  Pottery
  Building materials (Italy)
  Odor absorbents (cat litter)
  Oil drilling wells
http://manek.tradeindia.com/bentonite-all-grade-.html

## Slide 25: Modern Uses
Clay
  Pottery
  Building materials (Italy)
  Odor absorbents (cat litter)
  Oil drilling wells
  Land fill liner
http://pubs.sciepub.com/env/3/3/2/

## Slide 26: Modern Uses
Clay
  Pottery
  Building materials (Italy)
  Odor absorbents (cat litter)
  Oil drilling wells
  Land Fill Liner
  Dams
http://pubs.sciepub.com/env/3/3/2/

## Slide 27: Modern Uses of Clay
????

## Slide 28: Modern Uses of Clay
  Pottery
  Building materials (Italy)
  Odor absorbents (cat litter)
  Oil drilling wells
  Land Fill Liner
  Dams
  Gasoline production uses clay-based catalysts
  Paper making
  Hazardous waste clean-up
  Cement Production (1700’s used ground up Septarian Nodules which are clay and calcium carbonate to create a form of concrete)
  Chemical Filtering

## Slide 29: Extraterrestrial Clay?
Clay has been discovered on Mars
  Why is that important?

## Slide 30: Modern Uses Continued
Movies
https://www.youtube.com/watch?v=jVdlxwX6A7g